## Slide 1: — Scalable Networks for the ever evolving Student

## Slide 2: RMIT Wireless Pain-points
Legacy Core Wired Network
Legacy Wireless Network
Legacy Ancillary services – (Proxy Systems and Packet Shaper Systems)
Legacy Firewalls
Complex Topology
No Stability on Wireless Network
No enhanced services (EG: No Guest Wi-Fi)
Wireless Capacity and Coverage issues

## Slide 3: RMIT Wired Network
Old Nortel Wired Core Switches with limitations on ARP Table capability.
  Core CPU failures - RMIT faced service interruptions to environment.
  Legacy Wired Core Network replaced - Foundation laid to support ancillary services.
HP Routers “Wireless Core” was introduced to move wireless routing away from core network. (HP Routers were listed to support high ARP capability)

## Slide 4: RMIT Wireless Journey
Legacy Juniper Wireless required to be replaced, it was experiencing limitations at 16K user devices on the wireless network:
  1st Attempt – HP MSM did not scale.
  2nd Attempt – HP Unified Wireless, implementation stopped due to bugs/system instability.
  3rd Attempt – Aruba Wireless, Stable, Scalable Wireless Infrastructure and rolled out to entire campus.
  Was user experience issues resolved?
  The hope is yes.

## Slide 5: RMIT Wireless Journey
Natural increase in wireless devices per user – from 16K to 22K concurrent wireless devices in environment. (Over a 24hr period, 60K plus Unique devices).
  The HP 7900 Routers in the “Wireless Core” could not operate to the claim of high ARP capability.
  A different model 12900 HP Router was replaced to sustain the growth in number of devices and in turn support the ARP count. (128K if required).
In parallel RMIT replaced legacy firewall devices with Palo Alto Firewalls, causing bottle necks down stream.
  RMIT removed the legacy proxy device and traffic shapers from the environment and streamlined the network topology, removing all bottlenecks.

## Slide 6: RMIT Wireless Journey
RMIT wireless device increases to >30K concurrent unique devices.
  The Aruba software driver on the individual WAP was faulting at dense locations.
  Aruba released custom “Hotfix” for RMIT to resolve issue.
  Aruba built “Hotfix” into mainstream code and RMIT wireless upgraded.
  Was user experience issues finally resolved????? Yes !

## Slide 7: RMIT Wireless Capacity & Enhancements
Wireless Capacity |  |  | 
 | Max Capacity | Utilisation | Growth Capacity
Access Point | 6000 | 50% | 50%
Bandwidth | 60Gig | 10% | 90%
Concurrent Client | 100,000 | 26% | 74%
ARP Count | 128,000 | 20% | 80%
Wireless Guest Network Utilisation | 
 | Guest Numbers
Event Code | 9752
Sponsor Guest | 4653
Since September 2018

## Slide 8: RMIT Wireless Journey Summary
Wired core upgrade
Wireless core upgrade – 2 Attempts!
Wireless system upgrade – 3 Attempts – Aruba was the solution that provided stability!
Firewall system upgraded
Network topology streamlined and obsolete legacy devices decommissioned
Upgrade of the Aruba Wireless software
Introduction of Aruba Clear Pass (Profiling of Devices on the RMIT Network)
Enhancement to RMIT Wi-Fi (Guest Captive portal, Future IoT & Tuning Q1 2019)
Stable, Scalable, Flexible, Highly Available, Real Life Use Case Enhancement